## Slide 1
PYRamid level
  Subline
Date 09/13/2022
Name: NGUYEN LE KHAC ANH
Nguyen quang hung
R-car vision 2, soc sw,
VISION IP
Renesas Electronics Corporation

## Slide 2: Agenda
Overview Page 00
Frame Transformation Page 00
Coarse flow and Fine flow estimation Page 00
Backward and Forward flow field Page 00
Down-sampling and Up-sampling Page 00
Decoder – Tag and Encoder Page 00
Fusion Page 00

## Slide 3: Level Pyramid Diagram

## Slide 4: Overview
The UMF_CORE is designed in order to sequentially support optical flow estimation on different resolution levels of the same pairs of input images

## Slide 5: Frame Transformation
Frame transformation (FT) contains two identical blocks: FT_P is dedicated to process the previous
image frame, and FT_C is dedicated to process the current image
Feature: Smooth filtering of gray images

## Slide 6: Frame Transformation
A Gaussian Filter is a low-pass filter used for reducing noise (high-frequency components) and blurring regions of an image.

## Slide 7: Frame Transformation
A Gaussian Filter is a low-pass filter used for reducing noise (high-frequency components) and blurring regions of an image.
Original
Smooth

## Slide 8: The Gaussian FILTER
A 3x3 kernel filter with programmable coefficients is applied to the input gray image data
The input image consists of maximum 16 bits per pixel. In case of 12 bits/pixel, the 4 MSBs are unused. The programmable values of the filter coefficients PRE_SMC0-8 are 0, 1, 2, 4 and 8
Recommended coefficients values are
[0 0 0 0 1 0 0 0 0] : no smoothing
[1 2 1 2 4 2 1 2 1] : Gaussian filter
[1 1 1 1 1 1 1 1 1] : Box filter
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
3x3 kernel filter:

## Slide 9: Coarse Flow Estimation – Fine Flow Estimation
Seach range
Grid alignment

## Slide 10: Backward & Forward Flow Field
Backward flow field
Forward flow field

## Slide 11: Down-sampling and Up-sampling
The Gaussian Pyramid:
A representation in multiple scales
The goal is to define a representation in which image information at different scales is explicitly available

## Slide 12: Down-sampling and Up-sampling
1 | 2 | 3 | 4 | 5 | 6
7 | 8 | 9 | 10 | 11 | 12
13 | 14 | 15 | 16 | 17 | 18
19 | 20 | 21 | 22 | 23 | 24
25 | 26 | 27 | 28 | 29 | 30
31 | 32 | 33 | 34 | 35 | 36
1 | 3 | 5
13 | 15 | 17
25 | 27 | 29
Down-sampling and Up-sampling in DOF use the Gaussian pyramid method
Down-sampling
Notes: It makes the data of a more manageable size
Reduces the dimensionality of the data thus enabling in faster processing of the data (image)
Reducing the storage size of the data

## Slide 13: Down-sampling and Up-sampling
1 | 1 | 3 | 3 | 5 | 5
1 | 1 | 3 | 3 | 5 | 5
13 | 13 | 15 | 15 | 17 | 17
13 | 13 | 15 | 15 | 17 | 17
25 | 25 | 27 | 27 | 29 | 29
25 | 25 | 27 | 27 | 29 | 29
1 | 3 | 5
13 | 15 | 17
25 | 27 | 29
Down-sampling and Up-sampling in DOF use the Gaussian pyramid method
Up-sampling
Notes: It makes the data of a more manageable size
Reduces the dimensionality of the data thus enabling in faster processing of the data (image)
Reducing the storage size of the data

## Slide 14: Decoder – Tag (PCD + PLO) - Encoder
Input data formats
Output data formats
Decoder: The FUSION Decoder module decompresses, 10 bits each for U and V components, 2 bits for the flow encoding(FLE), 2 bits for pyramid level(PLO)and 1 bits for quality measure(PCD) by the Low Priority. The decompressed values are derived depending on the value of FLE by shifting both values by FLE bits to the left, the two FLE bits are then removed from the output.
Encoder: the pixel data is encoded back to the 32-bit compressed format used at the Path A input interface.

## Slide 15: Fusion
Decentralized Kalman filter
Evolution of the different variances
The FUSION module gets 2 flow-field estimate frames, and combines them into one resulting flow-field estimate frame, according to pixel based criteria, i.e., the output value is based locally only on the respective input values, not on their surrounding estimate values

## Slide 16: Kalman Filter
+ Q

## Slide 17: Dense Optical Flow OUTPUT
Flow field horizontal
Flow field vertical
Real world scenario
Single component flow fields
Red: negative component values with the brightness referring to the magnitude of the component
Green: positive component values with the brightness referring to the magnitude of the component

## Slide 18: Dense flow map result
Level maps(PLO)
Confirmation maps(PCD)

## Slide 19: Summary
Optical flow and fusion
No dedicated L1 flow field buffer, with L1 to L2 downscaling
Separate buffers, no L1 to L2 downscaling

## Slide 20: target application and algorithm
Lane Departure Warning(LDW)
Lane Keep Assist(LKA)
Lane Change Assist(LCA)
Autonomous Emergency Brake (AEB)
Forward Collision Warning (FCW)
Traffic Sign Recognition (TSR)
Intelligent Speed Assist (ISA)
High Beam Assist (HBA)
Traffic Jam Assist (TJA)
Night Vision(NV)
Traffic Signal Detection (TSD)
Lane maker
Traffic Sign Recognition (TSR)
Traffic Signal Detection (TSD)
Highway Pilot (HWP)
Speed
Performance
Dense-Stereo
Dense Optical-Flow
“Light”-Dense Optical-Flow
Structure from motion
(Visual) Ego-Motion
Clustering
Weak classifier (HOG,Hough)
Latent-SVM/DPM/Latent-CNN-Depp leaning
Random forest
Grid base SLAM
Planning
CNN-Deep leaning
TSR
Kalman-filter
Fusion
Deep Planning
High Speed Appli.
30-130km/h
Auto Parking Appli.
0-20km/h
Low Speed Appli.
0-80(130)km/h
HUD Appli.
0-80km/h
Auto Parking (APK)
Parking Area Detection (PSD)
Surround Monitoring System (SMS)
Base algorithm
Target application

## Slide 21: Data flow
Dense-
Stereo
Dense-
Optical-Flow
Camera
“Light”-Dense
Optical-Flow
Structure from motion
Planning
Strong classifier
(Visual) Ego-Motion
Clustering
Weak classifier
(HOG,Hough)
CNN-Deep leaning
TSR
Latent-SVM/ CNN(DPM)
Random forest
Kalman-filter
Grid base SLAM
Fusion
Tracking & environment
modeling
Planning
Planning
Strong classifier
CNN-Deep leaning
TSR
Kalman-filter
Fusion
Tracking & environment
modeling
Planning
Right
Camera
Left
Camera
“Light”-Dense
Optical-Flow
Structure from motion
(Visual) Ego-Motion
Clustering
Weak classifier
(HOG,Hough)
Deep Planning
Reliability
function
Reliability
function
Mono camera
Stereo camera or High end mono camera
[Option]

## Slide 22: Why need dense level ?
Vehicle control in sensitive scene
Become a very attractive sensing technique
for obtaining 3D information
3D information keep criteria targeted 130km/h

## Slide 23: Compare Dense to Sparse
Sparse
LK
Dense
Farneback
Renesas
(TVL1 base)
Flow Map
Convert arrow
Flow Map
Convert arrow

## Slide 24: Dense Map
IP | Target | Criteria
Dense-Optical-Flow | 2Mpix 16ms | 0-130Km/h High speed pilot
Dense-Stereo | 2Mpix 33ms | 0-130Km/h High speed pilot
Simulation result
Left image
Right image
Left +T image
Disparity map
Flow map
Hazard map
128
0
max
min
+
Disparity
Renesas Dense Map
Level
Flow

## Slide 25: Dense Map Simulation Demonstration

## Slide 26
Headline
  Subline